## Slide 1
Interrupts and Exceptions: Introduction
I. Ghansah
Revision date: 4/18/2021

## Slide 2: Interrupt Handling
Overview
Hardware Interrupts
Interrupt Control Instructions
Writing a Custom Interrupt Handler
Terminate and Stay Resident Programs
The No_Reset Program

## Slide 3: What is Interrupt?
It is an event that needs the CPU’s attention
CPU should stop whatever it is doing to service this interrupt before continuing from where it left off.
In practice a main program could be running and keyboard interrupt occurs (key has been pressed). We have to leave the main program and execute interrupt service routine (ISR) to collect the key that has been pressed, process it, and return control back to the main program.
In this sense ISR is similar to Procedure Call. But there are some differences.

## Slide 4: CPU Instruction Cycle with Interrupts
Fetch instruction at IP
Advance IP to next instruction
Decode the fetched instruction
Execute the decoded instruction
IRQ?
no
Save context
Get INTR ID
Lookup ISR
Execute ISR
yes
IRET
User
Program
IP
mov
add
mov
mul
mov
sub
bne
add
jmp
…

## Slide 5: INTERRUPT TYPES
Recall software Interrupts (eg. INT 21h, INT 10h calls). This instruction causes CPU to branch to Interrupt handler (same as ISR).
External Hardware Interrupts where an external device, not programmer, causes us to branch to interrupt handler.
  Keyboard interrupt which causes the PC to read a character pressed on the Keyboard.
  Ntwk Interface Card (NIC) for Wifi, Ethernet, etc.
  External Drives
  Printer
  …

## Slide 6: Some Types of Interrupts and Priorities (x86)
  Reset (Highest Priority)
  Internal Interrupts and Exceptions (divide by 0,
  Software Interrupts: (INT #)
  Non-Maskable Interrupts (NMI): External Hardware (memory read errors)
  External (maskable) Hardware, INTR (Lowest Priority). These are, KBD, NICs, HDD, etc

## Slide 7: Interrupt Vectors
All interrupts involve obtaining a vector (8 bit #) which is used by the CPU to fetch the address of the Interrupt Service Routine (ISR).
The address of the ISRs are in a table in memory beginning at 00h
Each entry (4B) in the table contains IP & CS of the corresponding ISR start address.

## Slide 8: Interrupt Vector Table
IP0
CS0
IP1
CS1
IP2
CS2
Vec 0 - divide error
Vec 1 - debug
Vec 2 - NMI
..
Vec 8 - PC Sys Timer OR interrupt table limit too small
Vec 9 - PC Keyboard
..
CS8
IP8
IP9
CS9
IP70h
CS70h
Vec 70h - CMOS Real Time Clock
..
Note: There is maximum of 256 vectors in Real Mode.
00
02
04
08
8*4
9*4
70h*4
Mem addr
Vector
Sys Services

## Slide 9: Hardware Requirements for Interrupts
MPU
Interrupt Controller
io1
io7
RAM
ROM
INT
INTA#
IR7
IR0
. . .
INTR
reset
NMI

## Slide 10: Interrupt Controller in x86 System
x86
CPU
Master
PIC
(8259)
Slave
PIC
(8259)
INTR
Programmable Interval-Timer
Keyboard Controller
Real-Time Clock
Legacy PC Design
(for single-proc
systems)
SCSI Disk
Ethernet
IRQs

## Slide 11: Overview
Interrupt handler (interrrupt service routine) – performs common I/O tasks
  can be called as functions
  can be activated by hardware events
Examples:
  video output handler
  critical error handler
  keyboard handler
  divide by zero handler
  Ctrl-Break handler
  serial port I/O

## Slide 12: Interrupt Vector Table
Each entry contains a 32-bit segment/offset address that points to an interrupt service routine
Offset = interruptNumber * 4
The following are only examples:

## Slide 13: Hardware Interrupts
Generated by the Intel 8259 Programmable Interrupt Contoller (PIC)
  in response to a hardware signal
Interrupt Request Levels (IRQ)
  priority-based interrupt scheduler
  brokers simultaneous interrupt requests
  prevents low-priority interrupt from interrupting a high-priority interrupt

## Slide 14: Common IRQ Assignments
0 System timer
1 Keyboard
2 Programmable Interrupt Controller
3 COM2 (serial)
4 COM1 (serial)
5 LPT2 (printer)
6 Floppy disk controller
7 LPT1 (printer)

## Slide 15: Common IRQ Assignments
8 CMOS real-time clock
9 modem, video, network, sound, and USB controllers
10 (available)
11 (available)
12 mouse
13 Math coprocessor
14 Hard disk controller
15 (available)

## Slide 16: Int 21H
Interrupt vector table
mov ...
Int 21H
Add ...
..
..
iret
..
..
iret
Your program
Interrupt handler
DOS
21H

## Slide 17: Interrupt
Interrupt vector table
mov ...
Add ...
..
..
iret
..
..
iret
Your program
Interrupt handler
Interrupt handler

## Slide 18: Hardware interrupt
Keyboard
interrupt
Your program

## Slide 19: Interrupts vs Procedure Calls
Similarities: In each case control is transferred to another routine
Differences
  CPU pushes flags, Return Address in that order whereas procedures pushes Ret Addr
  Interrupts use vector initially to know where to go
  Interrupt routines end with IRET( pops Ret Addr and flags from stack). RET used by procedures pops Ret Addr from the Stack

## Slide 20: Interrupt Control Instructions
STI – set interrupt flag
  enables external interrupts
  always executed at beginning of an interrupt handler
CLI – clear interrupt flag
  disables external interrupts
  used before critical code sections that cannot be interrupted
  suspends the system timer

## Slide 21: Writing a Custom Interrupt Handler
Motivations
  Change the behavior of an existing handler
  Fix a bug in an existing handler
  Improve system security by disabling certain keyboard commands
What's Involved
  Write a new handler
  Load it into memory
  Replace entry in interrupt vector table
  Chain to existing interrupt hander (usually)

## Slide 22: Setting up the Interrupt Vector Table
Place the address (es) of the ISR(s) at the places where the MPU can fetch them using the interrupt vector. NOTE: It’s a good idea to save an old Interrupt Vector before putting your own there. After you get out of the ISR, replace it.
The following code will save an old vector in kbd INT 9 (kbd hw intr)

## Slide 23: Saving Old ISR Info
Data segment use16
Oldoff dw ?
Oldseg dw ?
Data ends
Cli ; disable interrupts
Mov ax, 0000h ; ES=0
Mov es, ax
Mov bx, word ptr ES:24h ; save IP of INT 9 (kbd intr)
Mov oldoff, bx ;
Mov bx, word ptr ES:26h ; save CS of INT 9 (kbd intr)
Mov oldseg, bx

## Slide 24: Putting Own ISR Addr in IVT
Mov word ptr ES:24h, offset myISR
Mov word ptr ES:26h, seg myISR
sti
Where myISR is the address of my ISR

## Slide 25: Example Keyboard ISR
myISR:
Disable interrupts (CLI)
Save status with PUSHA (PUSH All gen. purpose regs)
Perform Service (eg. In case of KBD use IN AL, 60h)
Dismiss Interrupt (End of Interrupt (EOI) )
Enable Interrupts (STI)
Restore status with POPA
Return from Interrupt (IRET)
Dismissing interrupts can be done as follows.
Mov al, 20h ; Issue End Of Interrupt (EOI)
Out 20h, al ; To Master PIC port 20h

## Slide 26: Main Program
Must run in a Loop (preferably indefinite) in order to catch the Hardware Interrupt.

## Slide 27: Protected Mode Interrupts
Number of Interrupt Vector is unchanged from Real Mode. i.e still 256. The vector assignment is also the same.
Interrupt Vector Table (IVT) is called Interrupt Descriptor Table (IDT)
Entries in the IDT are 8 Bytes vs 4 Bytes in Real Mode. The entries are called Interrupt Gate Descriptors
The IDT can be anywhere in memory. It’s base address is in a CPU register called IDTR (IDT Register )
The actual address to the IVT is no longer 4*vector. Vector it multiplied by 8. But result goes to a GATE.

## Slide 28: Interrupt Descriptor Table
The ‘entry-point’ to the interrupt-handler is located via the Interrupt Descriptor Table (IDT)
IDT: “gate descriptors”
  Segment selector + offset for handler
  Descriptor Privilege Level (DPL)
  Gates (slightly different ways of entering kernel)
    Task gate: includes TSS to transfer to (not used by Linux)
    Interrupt gate: disables further interrupts
    Trap gate: further interrupts still allowed

## Slide 29: Interrupt Masking
Two different types: global and per-IRQ
Global — delays all interrupts
Selective — individual IRQs can be masked selectively
Selective masking is usually what’s needed — interference most common from two interrupts of the same type

## Slide 30: Protected Mode Interrupts
PIC
CPU
Memory Bus
INTR
0
N
IRQs
IDT
0
255
handler
idtr
Mask points
vector

## Slide 31: PROTECTED MODE INTERRUPT DETAILS
IDT
Interrupt Gate
Segment Descriptor
GDT
Interrupt Handler
+
Offset
Seg Selector
ISR
Destination Code Seg
IDTR
Interrupt Vector*8
+

## Slide 32
SKIP THE FOLLOWING: OPTIONAL

## Slide 33: Get Interrupt Vector
INT 21h Function 35h – Get interrupt vector
  returns segment-offset addr of handler in ES:BX
.data
int9Save LABEL WORD
DWORD ? ; store old INT 9 address here
.code
mov ah,35h ; get interrupt vector
mov al,9 ; for INT 9
int 21h ; call MS-DOS
mov int9Save,BX ; store the offset
mov [int9Save+2],ES ; store the segment

## Slide 34: Set Interrupt Vector
INT 21h Function 25h – Set interrupt vector
  installs new interrupt handler, pointed to by DS:DX
mov ax,SEG kybd_rtn ; keyboard handler
mov ds,ax ; segment
mov dx,OFFSET kybd_rtn ; offset
mov ah,25h ; set Interrupt vector
mov al,9h ; for INT 9h
int 21h
.
.
kybd_rtn PROC ; (new handler begins here)
See the CtrlBrk.asm program.

## Slide 35: Keyboard Processing Steps
Key pressed, byte sent by hardward to keyboard port
8259 controller interrupts the CPU, passing it the interrupt number
CPU looks up interrupt vector table entry 9h, branches to the address found there

## Slide 36: Keyboard Processing Steps
Our handler executes, intercepting the byte sent by the keyboard
Our handler jumps to the regular INT 9 handler
The INT 9h handler finishes and returns
System continues normal processing

## Slide 37: Terminate and Stay Resident Programs
(TSR): Installed in memory, stays there until removed
  by a removal program, or by rebooting
Keyboard example
  replace the INT 9 vector so it points to our own handler
  check, or filter certain keystroke combinations, using our handler
  forward-chain to the existing INT 9 handler to do normal keyboard processing

## Slide 38: The No_Reset Program (1 of 5)
Inspects each incoming key
If the Del key is received,
  checks for the Ctrl and Alt keys
  permits a system reset only if the Right shift key is also held down
The keyboard status byte indicates the current state of special keys:

## Slide 39: The No_Reset Program (2 of 5)
View the source code
Resident program begins with:
int9_handler PROC FAR
sti ; enable hardware interrupts
pushf ; save regs & flags
push es
push ax
push di

## Slide 40: The No_Reset Program (3 of 5)
Locate the keyboard flag byte and copy into AH:
L1: mov ax,40h ; DOS data segment is at 40h
mov es,ax
mov di,17h ; location of keyboard flag
mov ah,es:[di] ; copy keyboard flag into AH
Check to see if the Ctrl and Alt keys are held down:
L2: test ah,ctrl_key ; Ctrl key held down?
jz L5 ; no: exit
test ah,alt_key ; ALT key held down?
jz L5 ; no: exit

## Slide 41: The No_Reset Program (4 of 5)
Test for the Del and Right shift keys:
L3: in al,kybd_port ; read keyboard port
cmp al,del_key ; Del key pressed?
jne L5 ; no: exit
test ah,rt_shift ; right shift key pressed?
jnz L5 ; yes: allow system reset
Turn off the Ctrl key and write the keyboard flag byte back to memory:
L4: and ah,NOT ctrl_key ; turn off bit for CTRL
mov es:[di],ah ; store keyboard_flag

## Slide 42: The No_Reset Program (5 of 5)
Pop the flags and registers off the stack and execute a far jump to the existing BIOS INT 9h routine:
L5: pop di ; restore regs & flags
pop ax
pop es
popf
jmp cs:[old_interrupt9] ; jump to INT 9 routine

## Slide 43: What's Next
Defining Segments
Runtime Program Structure
Interrupt Handling
Hardware Control Using I/O Ports

## Slide 44: Hardware Control Using I/O Ports
Two types of hardware I/O
  memory mapped
    program and hardware device share the same memory address, as if it were a variable
  port based
    data written to port using the OUT instruction
    data read from port using the IN instruction

## Slide 45: Input-Ouput Ports
ports numbered from 0 to FFFFh
keyboard controller chip sends 8-bit scan code to port 60h
  triggers a hardware interrupt 9
IN and OUT instructions:
  IN accumulator, port
  OUT port, accumulator
  accumulator is AL, AX, or EAX
  port is a constant between 0 and FFh, or a value in DX betweeen 0 and FFFFh

## Slide 46: PC Sound Program
Generates sound through speaker
speaker control port: 61h
Intel 8255 Programmable Peripheral Interface chip turns the speaker on and off
Intel 8253 Timer chip controls the frequency
Source code

## Slide 47: Summary
Interrupt Intro: Priorities, Hardware Requirements
Interrupt handlers, interrupt vector table
Hardware interrupt, 8259 Programmable Interrupt Controller, interrupt flag
Protected Mode Interrupts.
Terminate and Stay Resident (TSR) – MAY SKIP
Memory-mapped and port-based I/O - SKIP

## Slide 48: The End