## Slide 1: Assembly Language for x86 Processors 7th Edition
Chapter 2: x86 Processor Architecture
(c) Pearson Education, 2015. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Dr. Isaac Ghansah
Revision date: 4/18/21
Kip Irvine

## Slide 2: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 3: Intel Microprocessor History
IA-16 processor family (Intel 8086)
IA-16 processor family (Intel 80286)
IA-32 processor family (Intel 80386, 80387)
IA-32 processor family (Intel 80486)
IA-32 processor family (Intel 80586, Pentium)
P6 processor family (Intel Pentium)
CISC and RISC

## Slide 4: Early Intel Microprocessors
Intel 8080
  64K addressable RAM
  8-bit registers
  CP/M operating system
  S-100 BUS architecture
  8-inch floppy disks!
Intel 8086/8088
  IBM-PC Used 8088
  1 MB addressable RAM
  16-bit registers
  16-bit data bus (8-bit for 8088)
  separate floating-point unit (8087)

## Slide 5: The IBM-AT
Intel 80286
  16 MB addressable RAM
  Protected memory
  several times faster than 8086
  introduced IDE bus architecture
  80287 floating point unit

## Slide 6: Intel IA-32 Family
Intel386
  4 GB addressable RAM, 32-bit registers, paging (virtual memory)
Intel486
  instruction pipelining
Pentium
  superscalar, 32-bit address bus, 64-bit internal data path

## Slide 7: Intel P6 Family
Pentium Pro
  advanced optimization techniques in microcode
Pentium II
  MMX (multimedia) instruction set
Pentium III
  SIMD (streaming extensions) instructions
Pentium 4 and Xeon
  Intel NetBurst micro-architecture, tuned for multimedia

## Slide 8: Detailed History of Intel Microprocessors
https://en.wikipedia.org/wiki/List_of_Intel_microprocessors

## Slide 9: CISC and RISC
CISC – complex instruction set computer
  large instruction set
  high-level operations
  requires microcode interpreter
  examples: Intel 80x86 family
RISC – reduced instruction set computer
  simple, atomic instructions
  small instruction set
  directly executed by hardware
  examples:
    ARM (Advanced RISC Machines)
    DEC Alpha (now Compaq)

## Slide 10: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 11: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing
Memory contains both instructions (code) and data
Special Register Program Counter (PC) contains address to next instruction. It is placed on the address bus to fetch instruction.

## Slide 12: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation. 1 Cycle time (Hz) = 1/clock speed (sec).
clock is used to trigger events
CPU speed is a function of clock speed.

## Slide 13: Memory and Access (Read/Write

## Slide 14: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 15: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output
Instruction Execution Cycle

## Slide 16: Reading from Memory
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  Place the address of the value you want to read on the address bus.
  Assert (changing the value of) the processor’s RD (read) pin.
  Wait one clock cycle for the memory chips to respond.
  Copy the data from the data bus into the destination operand
  NOTE: This is the reason why we want to avoid reading from memory if we can. Eg. Fewer instructions, more instructions executed inside CPU etc is better.

## Slide 17: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 18: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 19: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 20: Intel 965 Express Chipset

## Slide 21: Video Output
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required
* This link may change over time.

## Slide 22: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 23: Memory Hierarchy
Organized from the fastest to Slowest as follows
  Cache inside CPU (fastest, most cost/bit, volatile, smallest)
  Cache outside CPU
  RAM/ROM
  External Drive (SSD)
  External Drive (Hard Drive)
  Tape Drive (slowest, least cost/bit, non-volatile)

## Slide 24: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.
Cache is effective if the hit ratio is very high. This is true of programs in general because of loops.

## Slide 25: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly. Slower than SRAM
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required but power must be on all the time.
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information. Eg. Real-time clock
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 26: Memory Devices
Hard Disk Drive (HDD). Based on electromechanical technology. Non volatile.
Speed: 2.9 – 12 milliseconds (ms)
SSD (Solid State Drive). Based on electronic technology, a type of EEPROM, essentially flash technology. Faster but more expensive than HDD. Non volatile but data can leak data. Current trend is 20 yrs at 185 degree F to 100 years at 77 degree F

## Slide 27: I/O Devices

## Slide 28: Factors Affecting Input-Output (I/O) Devices
TECHNOLOGY: HDD is magnetic, DVD/CD is optical, KBD is mechanical, whereas MPU is electronic  Hardware INTERFACE NEEDED
DATA TRANSFER RATE Differences  Synchronization: Hardware/software concepts.
  Programmed I/O – rare today unless absolutely needed
  Interrupt I/O – KBD, mouse
  Direct Memory Access (DMA) – HDD, NICs, etc

## Slide 29: I/O Trends
CPU has n address lines, m data lines, and k control lines.
I/0 Devices interface is typically connected to a parallel bus to the CPU used to be connected with parallel lines (more recently printers)
Parallel require heavy expensive cables and physical connections to devices eg. Printers, kbd, etc.
Serial is uses 1 or sometimes 2 lines to transmit both (ie, address, data), extra lines for control, power and ground

## Slide 30: I/O Trends 2
Trend is towards serial because it is more cost effective. Ie. More bits per second over long distance at lower cost. Eg. USB, USB-C, HDMI, Firewire, SATA, DVI
Even buses are moving towards serial.
  PCI Express (PCIe)
Trend is towards Higher and Higher Speeds.
  HDMI: 4.9 – 48 Gbps
  USB: 1.5 Mbps (v1) – 10 Gbps (v3.1)

## Slide 31: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 32: Input-Output Ports (cont)
Serial (OLD)
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 33: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 34: Generic IO System Interface
CntrR
StatusR
DataR
External Decoder
Address
Data
R/W#
R/W#
CS
Register Select
Int Dcd
I/O Port
Int Bus
I/O Device
MPU
Bus

## Slide 35: How a Program Runs

## Slide 36: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 37: Modes of Operation
Protected mode
  native mode (Windows NT and later, Linux)
Real-address mode
  native MS-DOS, up to Windows ME
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 38: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 39: Addressable Memory
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 40: Floating-Point, MMX, XMM Registers
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations
SIMD = n processing elements (PE) with each PE performing the same operation on n data points simultaneously. Eg. Adjusting brightness in digital image or volume in audio. In general, vector operations using single instruction.

## Slide 41: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 42: IA-32 Memory Management
Real-address mode
Calculating linear addresses
Protected mode
Multi-segment model
Paging

## Slide 43: Protected Mode (1 of 2)
4 GB addressable RAM
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows (NT and later)

## Slide 44: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
Components of an IA-32 Microcomputer
Input-Output System

## Slide 45: 64-Bit Processors
64-Bit Operation Modes
  Compatibility mode – can run existing 16-bit and 32-bit applications (Windows supports only 32-bit apps in this mode)
  64-bit mode – Windows 64 uses this
Basic Execution Environment
  addresses can be 64 bits (48 bits, in practice)
  16 64-bit general purpose registers
  64-bit instruction pointer named RIP

## Slide 46: 64-Bit General Purpose Registers
32-bit general purpose registers:
  EAX, EBX, ECX, EDX, EDI, ESI, EBP, ESP, R8D, R9D, R10D, R11D, R12D, R13D, R14D, R15D
64-bit general purpose registers:
  RAX, RBX, RCX, RDX, RDI, RSI, RBP, RSP, R8, R9, R10, R11, R12, R13, R14, R15

## Slide 47: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
64-Bit Processors
x86 Architecture Trends
Input-Output System

## Slide 48: Computer Systems
●
Performance improvements:
●
●
Improvements in semiconductor technology
– Feature size, clock speed
Improvements in computer architectures
Enabled by high-level language compilers, general operating systems
Lead to RISC architectures
●
Together have enabled:
●
●
Lightweight computers
Productivity-based managed/interpreted programming languages

## Slide 49: Single CPU on-chip performance

## Slide 50: Points to note
●
●
●
The 52% growth per year is because of faster clock speeds and architectural innovations (led to 25x higher speed)
Clock speed increases have dropped to 1% per year in recent years
The 22% growth includes the parallelization from multiple cores
●
●
End of Moore’s Law: transistors on a chip double every 18-24 months

## Slide 51: Clock speed growth

## Slide 52: Current trends in architecture
●
Cannot continue to leverage Instruction-Level parallelism (ILP)
●
Single processor performance improvement ended in 2003
●
End of Moore’s Law

## Slide 53: n CPUs in 1 Socket
●
1 CPU socket
●
4 cores
2 logical (HT) threads each

## Slide 54: A simple 5-stage pipeline

## Slide 55: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 56: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 57: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 58: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 59: Summary
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Instruction execution cycle
Multitasking
Floating Point Unit (FPU)
Complex Instruction Set
Real mode and Protected mode
Motherboard components
Memory types
Input/Output and access levels

## Slide 60: The End