## Slide 1
Dr. Isaac Ghansah
Revision date: March 14, 2021
Conditional Processing
And
Control Structures
Chapter 6-A:

## Slide 2: Chapter Overview
Relational Operators
Comparison Instructions (cmp)
Conditional Jumps Instructions (Jcc)
Control Statements (Simple IF and WHILE)
Applications
Logical Instructions and Applications

## Slide 3: Relational operators
>
<
>=
<=
==
!=
Machine Instructions:
?

## Slide 4: CMP Instruction (1 of 3)
Compares the destination operand to the source operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax: CMP destination, source
Example: destination == source
mov al,5
cmp al,5 ; Zero flag set
Example: destination < source
mov al,4
cmp al,5 ; Carry flag set

## Slide 5: CMP Instruction (2 of 3)
Example: destination > source
mov al,6
cmp al,5 ; ZF = 0, CF = 0
(both the Zero and Carry flags are clear)

## Slide 6: CMP Instruction (3 of 3)
Example: destination > source
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
The comparisons shown here are performed with signed integers.
Example: destination < source
mov al,-1
cmp al,5 ; Sign flag != Overflow flag

## Slide 7: Conditional Jumps

## Slide 8: Conditional Jumps
Jumps Based On . . .
  Signed Comparisons
  Unsigned comparisons
  Specific flags
  CX or ECX
Applications
Encrypting a String
Bit Test (BT) Instruction

## Slide 9: Jcond Instruction
A conditional jump instruction branches to a label when specific register or flag conditions are met
Examples:
  JB, JC jump to a label if the Carry flag is set
  JE, JZ jump to a label if the Zero flag is set
  JS jumps to a label if the Sign flag is set
  JNE, JNZ jump to a label if the Zero flag is clear
  JECXZ jumps to a label if ECX equals 0

## Slide 10: Jcond Ranges
Prior to the 386:
  jump must be within –128 to +127 bytes from current location counter
IA-32 processors:
  32-bit offset permits jump anywhere in memory

## Slide 11: Relational Operators and Jcc Instructions
> | JG
< | JL
>= | JGE
<= | JLE
= = | JE
!= | JNE
Relational Operators Jcc Instructions
Note: Jumps Based on Signed Comparisons

## Slide 12: Note: Jumps Based on Unsigned Comparisons
> | JA
< | JB
>= | JAE
<= | JBE
= = | JE
!= | JNE
Relational Operators Jcc Instructions

## Slide 13: Jumps Based on Specific Flags
Instructions | Flags
JZ | ZF=1
JC | CF=1
JO | OF=1
JS | SF=1
JP | PF=1
Instructions | Flags
JNZ | ZF=0
JNC | CF=0
JNO | OF=0
JNS | SF=0
JNP | PF=0

## Slide 14: Jumps Based on CX or ECX
JCXZ L2 ;Jump if CX = 0
JECXZ L2 ;Jump if ECX = 0
JCXZ: Jump to a label if CX is zero
JECXZ: Jump to a label if ECX is zero
Examples:

## Slide 15: Applications (1 of 5)
cmp eax,ebx
ja Larger
Task: Jump to a label if unsigned EAX is greater than EBX
Solution: Use CMP, followed by JA
cmp eax,ebx
jg Greater
Task: Jump to a label if signed EAX is greater than EBX
Solution: Use CMP, followed by JG

## Slide 16: Applications (2 of 5)
cmp eax,Val1
jbe L1 ; below or equal
Jump to label L1 if unsigned EAX is less than or equal to Val1
cmp eax,Val1
jle L1
Jump to label L1 if signed EAX is less than or equal to Val1

## Slide 17: Applications (3 of 5)
  mov Large,bx
  cmp ax,bx
  jna Next
  mov Large,ax
Next:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
  mov Small,ax
  cmp bx,ax
  jnl Next
  mov Small,bx
Next:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small

## Slide 18: Applications (4 of 5)
  cmp WORD PTR [esi],0
  je L1
Jump to label L1 if the memory word pointed to by ESI equals Zero
test DWORD PTR [edi],1
jz L2
Jump to label L2 if the doubleword in memory pointed to by EDI is even

## Slide 19: Applications (5 of 5)
and al,00001011b ; clear unwanted bits
cmp al,00001011b ; check remaining bits
je L1 ; all set? jump to L1
Task: Jump to label L1 if bits 0, 1, and 3 in AL are all set.
Solution: Clear all bits except bits 0, 1,and 3. Then compare the result with 00001011 binary.

## Slide 20: Exercise . . .
Write code that jumps to label L1 if either bit 4, 5, or 6 is set in the BL register.
Write code that jumps to label L1 if bits 4, 5, and 6 are all set in the BL register.
Write code that jumps to label L2 if AL has even parity.
Write code that jumps to label L3 if EAX is negative.
Write code that jumps to label L4 if the expression (EBX – ECX) is greater than zero.

## Slide 21: Control Structures

## Slide 22: Control Structures
assignment statements
Loops: for loop statements
goto statements
If-else Statements
Compound Expressions with AND
Compound Expressions with OR
Loops: while Statements
Loops: do-while statement
break statements
continue statements
switch statements

## Slide 23: Simple IF Statement
If (val1 ==val2)
{
X=1;
Y=2;
}
Option 1
Mov eax,val1
Cmp eax,val2
Je L2
Jmp L1
L2:
Mov x, 1
Mov y, 2
L1:
Option 2
Mov eax,val1
Cmp eax,val2
Jne L1
Mov x, 1
Mov y, 2
L1:
Option 2 results in 1 less line of code. Can be significant depending on how many lines of code containing if statements

## Slide 24: Simple WHILE
While (val1<val2)
{
Val1++
Val2- -
}
L2:
OPTION 1
L1: mov eax,val1
cmp eax,val2
jb L3
jmp L2
L3: inc val1
dec val2
jmp L1
L2:
OPTION 2
L1: mov eax,val1
cmp eax,val2
jnb L2 ; false condition
inc val1
dec val2
jmp L1
L2:

## Slide 25: CMP Example – Lab 7
Get variable X from Keyboard. Ends with Enter Key (0dh)
Get variable Y from Keyboard. Ends with Enter Key (0dh)
Compute W
Output W
Prompt to continue or quit
If continue Go to step 1 else Exit

## Slide 26: Lab 7 Hints - continued
.data
…
.code
Main PROC
…
Mov esi, offset InputX ;input parameter passing
Call GetInput
Mov X,eax ;output parameter passing
Mov esi, offset InputY
Call GetInput
Mov Y,eax
Mov esi,X ;input parameter passing
Mov edi,Y ; input parameter passing
Call calculateW
Mov W, eax ;output
…
Main ENDP

## Slide 27: CMP IN LAB 7 – Session loop & checking for ‘q’ key to quit
.data
…
.code
Main PROC
…
Top: Mov esi, offset InputX ;input
Call GetInput
Mov X,eax ;output
Mov esi, offset InputY
Call GetInput
Mov Y,eax ;output
Mov esi,X ;input parameter
Mov edi,Y ;input parameter
Call calculateW
Mov W, eax ;output
…
…
Call ReadChar ;read KBD
Call Writechar ;echo
Cmp al, ‘q’
Jne top
…
Main ENDP

## Slide 28: CMP IN LAB 7 –checking for ENTER key to end number
GetInput PROC
…
L1:
...
Call readchar
Call writechar
Cmp al, 0dh
Je L2
Sub al,30h
…
…
Jmp L1
L2: prepare to exit
…
…
Ret
GetInput ENDP

## Slide 29
Chapter 6-A:
Part 2
Logical Instructions
AND, OR, NOT, XOR, TEST
7

## Slide 30: Chapter Overview
Logical Instructions
JMP and LOOP Instructions (4.5)
Conditional Loop Instructions
Stack and Stack Operations (5.4)

## Slide 31: Logical (Boolean) Instructions
Operators Instructions
& and
| or
! not
xor

## Slide 32: Boolean and Comparison Instructions
CPU Status Flags
AND Instruction
OR Instruction
XOR Instruction
NOT Instruction
Applications
TEST Instruction
CMP Instruction

## Slide 33: Status Flags - Review
The Zero flag is set when the result of an operation equals zero.
The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.
The Overflow flag is set when an instruction generates an invalid signed result (bit 7 carry is XORed with bit 6 Carry).
The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
The Auxiliary Carry flag is set when an operation produces a carry out from bit 3 to bit 4

## Slide 34: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands
Syntax:
    AND destination, source (same operand types as MOV)
Properties: x.y=1 only if x=1 and y=1. Else 0
x.1 = x; Identity. x.0 = 0; Masking
Can be used to test if a value is 1
Code: MOV al,3bh. AND al,0fh
AND

## Slide 35: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands
Syntax: OR destination, source
Properties: x+y= 0 only if x=0 and y=0 Else 1
X+1 = 1; Force 1. x+0 = x; Identity
Can be used to test if a value is 0
Code: MOV al,3bh. OR al,0fh
OR

## Slide 36: NOT Instruction
Performs a Boolean NOT operation on a single destination operand
Syntax: NOT destination
Property: NOT is used to Toggle.
Note that NEG x = (NOT x )+ 1.
Mov al, 0fh
Not al; al; al =0c4h
Mov al 0fh
Neg al; al = 0c5h
NOT

## Slide 37: XOR Instruction
Performs a Boolean exclusive-OR operation between each pair of matching bits in two operands
Syntax: XOR destination, source
Properties: x xor y = 1 if x not y OR y not x; Unequal
x xor y =0 if x=y: Equal
ie. x xor x = 0; y xor y =0; Clear
If x=0, 0 xor y =y ; Passthrough
if x=1, 1 xor y = y’ ; Toggle (Invert)
XOR

## Slide 38: More on XOR
Consider the Properties
  x xor 0 = x
  x xor 1 = x’ = NOT x ; Inversion
  x xor x =0;
It means
  Xor eax, 0; eax does not change. Not of much use
  Xor eax, 0ffffh; not eax. Each bit is inverted
  Xor eax, eax ; eax =0 ie can be used to clear a register. This is faster than mov eax,0

## Slide 39: XOR IN SYMMETRIC KEY CRYPTOGRAPHY
Assume principals (people, machines, etc) A and B share a secret key which can be used to both encrypt to decrypt (symmetric)
A computes c= x xor k and sends to B. This is encryption
When B receives c, B uses the same secret key k to computes c xor k
Notice that c xor k = (x xor k) xor k =x xor k xor k
We know that k xor k = 0. Thus c xor k = x xor o =x
In a real application A performs xor eax, key to encrypt and B performs xor eax, key to decrypt

## Slide 40: Applications (1 of 4)
mov al,'a' ; AL = 01100001b
and al,11011111b ; AL = 01000001b
Task: Convert the character in AL to upper case.
Solution: Use the AND instruction to clear bit 5.

## Slide 41: Applications (2 of 4)
mov al,6 ; AL = 00000110b
or al,00110000b ; AL = 00110110b
Task: Convert a binary decimal byte into its equivalent ASCII decimal digit.
Solution: Use the OR instruction to set bits 4 and 5.
The ASCII digit '6' = 00110110b

## Slide 42: Applications (3 of 4)
mov ax,wordVal
and ax,1 ; low bit set?
jz EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.
JZ (jump if Zero) is covered in Section 6.3.
Your turn: Write code that jumps to a label if an integer is negative.

## Slide 43: Applications (4 of 4)
or al,al
jnz IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 44: Encrypting a String
KEY = 239 ; can be any byte value
BUFMAX = 128
.data
buffer BYTE BUFMAX+1 DUP(0)
bufSize DWORD BUFMAX
.code
  mov ecx,bufSize ; loop counter
  mov esi,0 ; index 0 in buffer
L1:
  xor buffer[esi],KEY ; translate a byte
  inc esi ; point to next byte
  loop L1
The following loop uses the XOR instruction to transform every character in a string into a new value.

## Slide 45: String Encryption Program
Tasks:
  Input a message (string) from the user
  Encrypt the message
  Display the encrypted message
  Decrypt the message
  Display the decrypted message
View the Encrypt.asm program's source code. Sample output:
Enter the plain text: Attack at dawn.
Cipher text: «¢¢Äîä-Ä¢-ïÄÿü-Gs
Decrypted: Attack at dawn.

## Slide 46: TEST Instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the Zero flag is affected.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
test al,00000011b
jnz ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
test al,00000011b
jz ValueNotFound

## Slide 47: TEST Instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the Zero flag is affected.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
test al,00000011b
jnz ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
test al,00000011b
jz ValueNotFound

## Slide 48: BT (Bit Test) Instruction
Copies bit n from an operand into the Carry flag
Syntax: BT bitBase, n
  bitBase may be r/m16 or r/m32
  n may be r16, r32, or imm8
Example: jump to label L1 if bit 9 is set in the AX register:
bt AX,9 ; CF = bit 9
jc L1 ; jump if Carry

## Slide 49: Boolean Instructions in 64-Bit Mode
64-bit boolean instructions, for the most part, work the same as 32-bit instructions
If the source operand is a constant whose size is less than 32 bits and the destination is the lower part of a 64-bit register or memory operand, all bits in the destination operand are affected
When the source is a 32-bit constant or register, only the lower 32 bits of the destination operand are affected

## Slide 50: The End