## Slide 1
Dr. Isaac Ghansah
Revision date: April 1, 2020
Conditional Processing
Compound Control Structures
Chapter 6-B:

## Slide 2: Chapter Overview
Advanced Control Statements and Optimization
  If cond1 then ... Else …
  If cond1 AND cond2 ,.,.
  If cond1 OR cond2 …
  While with break, continue, etc
  …

## Slide 3: If then Else Statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  mov eax,var1
  cmp eax,var2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( var1 == var2 )
X = 1;
else
X = 2;

## Slide 4: Exercise – Optimized If Statement
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 5: Exercise – If then Else
Implement the following pseudocode in assembly language. All values are 32-bit signed integers:
  mov eax,var1
  cmp eax,var2
  jle L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)

## Slide 6: Compound Expression with AND (1 of 3)
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped: This is based on the AND property that A.B = 0 if one them is 0.
a1, b1, and c1 are variables
if (a1 > b1) AND (b1 > c1)
X = 1;

## Slide 7: Compound Expression with AND (2 of 3)
mov eax,a1
cmp eax,b1 ;1st expression. True?
ja L1
jmp next
L1:
mov eax,b1
cmp eax,c1 ;2nd expression. True?
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
if (a1 > b1) AND (b1 > c1)
X = 1;
Next:…
Option 1: 9 lines of Code.

## Slide 8: Compound Expression with AND (3 of 3)
mov eax,a1
cmp eax,b1 ;1st expression. False?
jbe next ; quit if false
mov eax,b1
cmp eax,c1 ;2nd expression. False?
jbe next ; quit if false
mov X,1 ; both are true
next:
if (a1 > b1) AND (b1 > c1)
X = 1;
Next: …
Option 2: Optimized; 7 lines of Code
The following implementation uses 2 less lines of code by reversing the first relational operator. This allows the program to "fall through" to the second expression. This approach has been used before for simple IF and WHILE statements:

## Slide 9: Exercise . . .
Implement the following pseudocode in assembly language. All values are unsigned: Optimal Solution
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 10: Compound Expression with OR (1 of 3)
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is true, the second expression is skipped. This is based on the fact that 1+B =1
if (a1 > b1) OR (b1 > c1)
X = 1;

## Slide 11
Dr. Isaac Ghansah
11
Compound Expression with OR (2 of 3)
mov eax,a1
cmp eax,b1 ; is a1 > b1?
ja L1 ; yes, X=1; DONE
mov eax,b1
cmp eax,c1 ; If not: is b1 > c1?
ja L1 ;Yes, X=1; Done
jmp next ; no: both false. SKIP
L1: mov X,1 ; set X to 1
next:
if (a1 > b1) OR (b1 > c1)
X = 1;
Option 1: 8 lines

## Slide 12: Compound Expression with OR (1 of 3)
mov eax,a1
cmp eax,b1 ; is A1 > B1?
ja L1 ; yes; Done
mov eax,b1 ;
cmp eax,c1 ; no: is B1 > C1?
jbe next ; no: Both false so Skip
L1: mov X,1 ; set X to 1
next:
if (a1 > b1) OR (b1 > c1)
X = 1;
Option 2: Optimized. 7 lines. We can use "fall-through" logic to keep the code as short as possible:

## Slide 13: WHILE Loops
while( eax < ebx)
eax = eax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:
top: cmp eax,ebx ; check loop condition
jae next ; false? exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:

## Slide 14: Exercise – While … Do
top: cmp ebx,val1 ; check loop condition
ja next ; false? exit loop
add ebx,5 ; body of loop
dec val1
jmp top ; repeat the loop
next:
while( ebx <= val1)
{
ebx = ebx + 5;
val1 = val1 - 1
}
Implement the following WHILE loop, using unsigned 32-bit integers:

## Slide 15: Do-While (Repeat-Until) Loops
do
eax = eax + 1;
while( eax <= ebx);
A do-while loop is really a while loop with condition checked at the end of the loop. That is, Loop executes at least once Consider the following example:
top: inc eax ; body of loop
cmp eax,ebx ; check loop condition
jle top ; false? exit loop
next:
This is a possible implementation:

## Slide 16: break statements . . .
top: cmp ebx,1000 ; check loop condition
jg out ; true? exit loop
add ebx,5 ; body of loop
jmp top ; repeat the loop
out:
while( 1 )
{
if (ebx > 1000) break;
ebx = ebx + 5;
}
Implement the following loop, using unsigned 32-bit integers:

## Slide 17: continue statements . . .
top: cmp ebx,val1 ; check loop condition
ja next ; false? exit loop
add ebx,5 ; body of loop
cmp ebx,1000 ; check condition
jl top ; true? continue
dec val1
jmp top ; repeat the loop
next:
while( ebx <= val1)
{
ebx = ebx + 5;
if (ebx < 1000) continue; Skip and goto top
val1 = val1 - 1
}

## Slide 18: switch statements (1 of 2)
switch statement is just an if-else statements
Suited to a small number of comparisons

## Slide 19: switch statements (2 of 2)
switch statement uses a table lookup to replace a multiway selection structure
Create a table containing lookup values and the offsets of labels or procedures
Use a loop to search the table
Suited to a large number of comparisons

## Slide 20: Table-Driven Selection (1 of 4)
Table-driven selection uses a table lookup to replace a multiway selection structure
Create a table containing lookup values and the offsets of labels or procedures
Use a loop to search the table
Suited to a large number of comparisons

## Slide 21: Table-Driven Selection (2 of 4)
.data
CaseTable BYTE 'A' ; lookup value
DWORD Process_A ; address of procedure
EntrySize = ($ - CaseTable)
BYTE 'B'
DWORD Process_B
BYTE 'C'
DWORD Process_C
BYTE 'D'
DWORD Process_D
NumberOfEntries = ($ - CaseTable) / EntrySize
Step 1: create a table containing lookup values and procedure offsets:

## Slide 22: Table-Driven Selection (3 of 4)
Table of Procedure Offsets:

## Slide 23: Table-Driven Selection (4 of 4)
mov ebx,OFFSET CaseTable ; point EBX to the table
mov ecx,NumberOfEntries ; loop counter
L1: cmp al,[ebx] ; match found?
jne L2 ; no: continue
call NEAR PTR [ebx + 1] ; yes: call the procedure
call WriteString ; display message
call Crlf
jmp L3 ; and exit the loop
L2: add ebx,EntrySize ; point to next entry
loop L1 ; repeat until ECX = 0
L3:
Step 2: Use a loop to search the table. When a match is found, call the procedure offset stored in the current table entry:
required for procedure pointers

## Slide 24: Summary
JMP and LOOP – branching instructions
PUSH and POP instructions
Bitwise instructions (AND, OR, XOR, NOT, TEST)
  manipulate individual bits in operands
CMP – compares operands using implied subtraction
  sets condition flags
Conditional Jumps & Loops
  equality: JE, JNE
  flag values: JC, JZ, JNC, JP, ...
  signed: JG, JL, JNG, ...
  unsigned: JA, JB, JNA, ...
  IF,WHILE, compound control, break, continue, switch, etc implementations

## Slide 25: The End