## Slide 1: Assembly Language for x86 Processors 7th Edition
Chapter 9: Strings Instructions and Arrays
(c) Pearson Education, 2015. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Dr. I. Ghansah
Revision date: 4/17/2020
Kip R. Irvine

## Slide 2: Chapter Overview
String Instructions
Selected String Procedures (Optional s20)
Two-Dimensional Arrays (Optional s20)

## Slide 3: String Primitive Instructions
MOVSB, MOVSW, and MOVSD
CMPSB, CMPSW, and CMPSD
SCASB, SCASW, and SCASD
STOSB, STOSW, and STOSD
LODSB, LODSW, and LODSD

## Slide 4: MOVSB, MOVSW, and MOVSD (1 of 2)
The MOVSB, MOVSW, and MOVSD instructions copy data from the memory location pointed to by ESI to the memory location pointed to by EDI.
.data
source DWORD 0FFFFFFFFh
target DWORD ?
.code
mov esi,OFFSET source
mov edi,OFFSET target
Movsd ;

## Slide 5: MOVSB, MOVSW, and MOVSD (2 of 2)
ESI and EDI are automatically incremented or decremented:
  MOVSB increments/decrements by 1
  MOVSW increments/decrements by 2
  MOVSD increments/decrements by 4

## Slide 6: Direction Flag
The Direction flag controls the incrementing or decrementing of ESI and EDI.
  DF = clear (0): increment ESI and EDI
  DF = set (1): decrement ESI and EDI
The Direction flag can be explicitly changed using the CLD and STD instructions:
CLD ; clear Direction flag
STD ; set Direction flag

## Slide 7: Using a Repeat Prefix
REP (a repeat prefix) can be inserted just before MOVSB, MOVSW, or MOVSD.
ECX controls the number of repetitions
Example: Copy 20 doublewords from source to target
.data
source DWORD 20 DUP(?)
target DWORD 20 DUP(?)
.code
cld ; direction = forward
mov ecx,LENGTHOF source ; set REP counter
mov esi,OFFSET source
mov edi,OFFSET target
rep movsd

## Slide 8
.data
source DWORD 20 DUP(?)
target DWORD 20 DUP(?)
.code
cld
mov ecx,LENGTHOF source
mov esi,OFFSET source
mov edi,OFFSET target
rep movsd
data
source DWORD 20 DUP(?)
target DWORD 20 DUP(?)
.code
cld
mov ecx,LENGTHOF source
mov esi,OFFSET source
mov edi,OFFSET target
L1:
Mov al, [esi]
Mov [edi], al
Add esi, 4
Add edi, 4
Loop L1

## Slide 9: Your turn . . .
Use MOVSD to delete the first element of the following doubleword array. All subsequent array values must be moved one position forward toward the beginning of the array:
  array DWORD 1,1,2,3,4,5,6,7,8,9,10
.data
array DWORD 1,1,2,3,4,5,6,7,8,9,10
.code
cld
mov ecx,(LENGTHOF array) - 1
mov esi,OFFSET array+4
mov edi,OFFSET array
rep movsd

## Slide 10: CMPSB, CMPSW, and CMPSD
The CMPSB, CMPSW, and CMPSD instructions each compare a memory operand pointed to by ESI to a memory operand pointed to by EDI.
  CMPSB compares bytes
  CMPSW compares words
  CMPSD compares doublewords
Repeat prefix often used
  REPE (REPZ)
  REPNE (REPNZ)

## Slide 11: Comparing a Pair of Doublewords
.data
source DWORD 1234h
target DWORD 5678h
.code
mov esi,OFFSET source
mov edi,OFFSET target
cmpsd ; compare doublewords
ja L1 ; jump if source > target
jmp L2 ; jump if source <= target
If source > target, the code jumps to label L1; otherwise, it jumps to label L2

## Slide 12: Your turn . . .
Modify the program in the previous slide by declaring both source and target as WORD variables. Make any other necessary changes.

## Slide 13: Comparing Arrays
.data
source DWORD COUNT DUP(?)
target DWORD COUNT DUP(?)
.code
mov ecx,COUNT ; repetition count
mov esi,OFFSET source
mov edi,OFFSET target
cld ; direction = forward
repe cmpsd ; repeat while equal
Use a REPE (repeat while equal) prefix to compare corresponding elements of two arrays.

## Slide 14: Example: Comparing Two Strings (1 of 3)
.data
source BYTE "MARTIN "
dest BYTE "MARTINEZ"
str1 BYTE "Source is smaller",0dh,0ah,0
str2 BYTE "Source is not smaller",0dh,0ah,0
This program compares two strings (source and destination). It displays a message indicating whether the lexical value of the source string is less than the destination string.
Source is smaller
Screen output:

## Slide 15: Example: Comparing Two Strings (2 of 3)
.code
main PROC
  cld ; direction = forward
  mov esi,OFFSET source
  mov edi,OFFSET dest
  mov ecx,LENGTHOF source
  repe cmpsb
  jb source_smaller
  mov edx,OFFSET str2 ; "source is not smaller"
  jmp done
source_smaller:
  mov edx,OFFSET str1 ; "source is smaller"
done:
  call WriteString
  exit
main ENDP
END main

## Slide 16: Example: Comparing Two Strings (3 of 3)
The following diagram shows the final values of ESI and EDI after comparing the strings:

## Slide 17: SCASB, SCASW, and SCASD
The SCASB, SCASW, and SCASD instructions compare a value in AL/AX/EAX to a byte, word, or doubleword, respectively, addressed by EDI.
Useful types of searches:
  Search for a specific element in a long string or array.
  Search for the first element that does not match a given value.

## Slide 18: SCASB Example
.data
alpha BYTE "ABCDEFGH",0
.code
mov edi,OFFSET alpha
mov al,'F' ; search for 'F'
mov ecx,LENGTHOF alpha
cld
repne scasb ; repeat while not equal
jnz quit
dec edi ; EDI points to 'F'
Search for the letter 'F' in a string named alpha:
What is the purpose of the JNZ instruction?

## Slide 19: STOSB, STOSW, and STOSD
The STOSB, STOSW, and STOSD instructions store the contents of AL/AX/EAX, respectively, in memory at the offset pointed to by EDI.
Example: fill an array with 0FFh. Ie. erase, initialize, ..
.data
Count = 100
string1 BYTE Count DUP(?)
.code
mov al,0FFh ; value to be stored
mov edi,OFFSET string1 ; ES:DI points to target
mov ecx,Count ; character count
cld ; direction = forward
rep stosb ; fill with contents of AL

## Slide 20: LODSB, LODSW, and LODSD
LODSB, LODSW, and LODSD load a byte or word from memory at ESI into AL/AX/EAX, respectively.
Example: Collect numbers from memory and display on screen.
.data
array BYTE 1,2,3,4,5,6,7,8,9
.code
mov esi,OFFSET array
mov ecx,LENGTHOF array
cld
L1: lodsb ; load byte into AL
or al,30h ; convert to ASCII
call WriteChar ; display it
loop L1

## Slide 21: Array Multiplication Example
.data
array DWORD 1,2,3,4,5,6,7,8,9,10
multiplier DWORD 10
.code
cld ; direction = up
mov esi,OFFSET array ; source index
mov edi,esi ; destination index
mov ecx,LENGTHOF array ; loop counter
L1: lodsd ; copy [ESI] into EAX
mul multiplier ; multiply by a value
stosd ; store EAX at [EDI]
loop L1
Multiply each element of a doubleword array by a constant value.

## Slide 22: Your turn . . .
Write a program that converts each unpacked binary-coded decimal byte belonging to an array into an ASCII decimal byte and copies it to a new array.
mov esi,OFFSET array
mov edi,OFFSET dest
mov ecx,LENGTHOF array
cld
L1: lodsb ; load into AL
or al,30h ; convert to ASCII
stosb ; store into memory
loop L1
.data
array BYTE 1,2,3,4,5,6,7,8,9
dest BYTE (LENGTHOF array) DUP(?)

## Slide 23: THE END for Spring 2020

## Slide 24: What's Next
String Primitive Instructions
Selected String Procedures
Two-Dimensional Arrays
Searching and Sorting Integer Arrays

## Slide 25: Selected 32-Bit String Procedures
Str_compare Procedure
Str_length Procedure
Str_copy Procedure
Str_trim Procedure
Str_ucase Procedure
The following string procedures may be found in the Irvine32 library

## Slide 26: Str_compare Procedure
Compares string1 to string2, setting the Carry and Zero flags accordingly
Prototype:
Str_compare PROTO,
string1:PTR BYTE, ; pointer to string
string2:PTR BYTE ; pointer to string

## Slide 27: Str_compare Source Code
Str_compare PROC USES eax edx esi edi,
string1:PTR BYTE, string2:PTR BYTE
mov esi,string1
mov edi,string2
L1: mov al,[esi]
mov dl,[edi]
cmp al,0 ; end of string1?
jne L2 ; no
cmp dl,0 ; yes: end of string2?
jne L2 ; no
jmp L3 ; yes, exit with ZF = 1
L2: inc esi ; point to next
inc edi
cmp al,dl ; chars equal?
je L1 ; yes: continue loop
L3: ret
Str_compare ENDP

## Slide 28: Str_length Procedure
Calculates the length of a null-terminated string and returns the length in the EAX register.
Prototype:
.data
myString BYTE "abcdefg",0
.code
INVOKE Str_length,
ADDR myString
; EAX = 7
Example:
Str_length PROTO,
pString:PTR BYTE ; pointer to string

## Slide 29: Str_length Source Code
Str_length PROC USES edi,
pString:PTR BYTE ; pointer to string
mov edi,pString
mov eax,0 ; character count
L1:
cmp byte ptr [edi],0 ; end of string?
je L2 ; yes: quit
inc edi ; no: point to next
inc eax ; add 1 to count
jmp L1
L2: ret
Str_length ENDP

## Slide 30: Str_copy Procedure
Copies a null-terminated string from a source location to a target location.
Prototype:
See the CopyStr.asm program for a working example.
Str_copy PROTO,
source:PTR BYTE, ; pointer to string
target:PTR BYTE ; pointer to string

## Slide 31: Str_copy Source Code
Str_copy PROC USES eax ecx esi edi,
source:PTR BYTE, ; source string
target:PTR BYTE ; target string
INVOKE Str_length,source ; EAX = length source
mov ecx,eax ; REP count
inc ecx ; add 1 for null byte
mov esi,source
mov edi,target
cld ; direction = up
rep movsb ; copy the string
ret
Str_copy ENDP

## Slide 32: Str_trim Procedure
The Str_trim procedure removes all occurrences of a selected trailing character from a null-terminated string.
Prototype:
Str_trim PROTO,
pString:PTR BYTE, ; points to string
char:BYTE ; char to remove
.data
myString BYTE "Hello###",0
.code
INVOKE Str_trim, ADDR myString, '#'
myString = "Hello"
Example:

## Slide 33: Str_trim Procedure
Str_trim checks a number of possible cases (shown here with # as the trailing character):
  The string is empty.
  The string contains other characters followed by one or more trailing characters, as in "Hello##".
  The string contains only one character, the trailing character, as in "#"
  The string contains no trailing character, as in "Hello" or "H".
  The string contains one or more trailing characters followed by one or more nontrailing characters, as in "#H" or "###Hello".

## Slide 34: Testing the Str_trim Procedure
Using the first definition in the table, position of EDI when SCASB stops:

## Slide 35: Str_trim Source Code
Str_trim PROC USES eax ecx edi,
pString:PTR BYTE, ; points to string
char:BYTE ; char to remove
mov edi,pString
INVOKE Str_length,edi ; returns length in EAX
cmp eax,0 ; zero-length string?
je L2 ; yes: exit
mov ecx,eax ; no: counter = string length
dec eax
add edi,eax ; EDI points to last char
mov al,char ; char to trim
std ; direction = reverse
repe scasb ; skip past trim character
jne L1 ; removed first character?
dec edi ; adjust EDI: ZF=1 && ECX=0
L1: mov BYTE PTR [edi+2],0 ; insert null byte
L2: ret
Str_trim ENDP

## Slide 36: Str_ucase Procedure
The Str_ucase procedure converts a string to all uppercase characters. It returns no value.
Prototype:
Str_ucase PROTO,
pString:PTR BYTE ; pointer to string
.data
myString BYTE "Hello",0
.code
INVOKE Str_ucase,
ADDR myString
Example:

## Slide 37: Str_ucase Source Code
Str_ucase PROC USES eax esi,
pString:PTR BYTE
mov esi,pString
L1: mov al,[esi] ; get char
cmp al,0 ; end of string?
je L3 ; yes: quit
cmp al,'a' ; below "a"?
jb L2
cmp al,'z' ; above "z"?
ja L2
and BYTE PTR [esi],11011111b ; convert the char
L2: inc esi ; next char
jmp L1
L3: ret
Str_ucase ENDP

## Slide 38: String Procedures in the Irvine64 Library
Str_compare – compares two strings pointed to by RSI and RDI. Sets the Carry and Zero flags in the same manner as the CMP instruction
Str_copy – copies a source string to a location identified by a target pointer
Str_length – returns the length of a null-terminated string

## Slide 39: Example: 64-Bit Str_length
Gets the length of a string. Receives: RCX points to the string. Returns length of string in RAX.
Str_length PROC USES rdi
mov rdi,rcx ; get pointer
mov eax,0 ; character counter
L1:
cmp BYTE PTR [rdi],0 ; end of string?
je L2 ; yes: quit
inc rdi ; no: point to next
inc rax ; add 1 to count
jmp L1
L2: ret ; return count in RAX
Str_length ENDP

## Slide 40: What's Next
String Primitive Instructions
Selected String Procedures
Two-Dimensional Arrays
Searching and Sorting Integer Arrays

## Slide 41: Two-Dimensional Arrays
Base-Index Operands
Base-Index Displacement

## Slide 42: Base-Index Operand
A base-index operand adds the values of two registers (called base and index), producing an effective address. Any two 32-bit general-purpose registers may be used. (Note: esp is not a general-purpose register)
  In 64-bit mode, you use 64-bit registers for bases and indexes
Base-index operands are great for accessing arrays of structures. (A structure groups together data under a single name. )

## Slide 43: Structure Application
A common application of base-index addressing has to do with addressing arrays of structures (Chapter 10). The following defines a structure named COORD containing X and Y screen coordinates:
COORD STRUCT
X WORD ? ; offset 00
Y WORD ? ; offset 02
COORD ENDS
.data
setOfCoordinates COORD 10 DUP(<>)
Then we can define an array of COORD objects:

## Slide 44: Structure Application
The following code loops through the array and displays each Y-coordinate:
mov ebx,OFFSET setOfCoordinates
mov esi,2 ; offset of Y value
mov eax,0
L1: mov ax,[ebx+esi]
call WriteDec
add ebx,SIZEOF COORD
loop L1

## Slide 45: Base-Index-Displacement Operand
A base-index-displacement operand adds base and index registers to a constant, producing an effective address. Any two 32-bit general-purpose register can be used.
Common formats:
[ base + index + displacement ]
displacement [ base + index ]

## Slide 46: 64-bit Base-Index-Displacement Operand
A 64-bit base-index-displacement operand adds base and index registers to a constant, producing a 64-bit effective address. Any two 64-bit general-purpose registers can be used.
Common formats:
[ base + index + displacement ]
displacement [ base + index ]

## Slide 47: Two-Dimensional Table Example
Imagine a table with three rows and five columns. The data can be arranged in any format on the page:
table BYTE 10h, 20h, 30h, 40h, 50h
BYTE 60h, 70h, 80h, 90h, 0A0h
BYTE 0B0h, 0C0h, 0D0h, 0E0h, 0F0h
NumCols = 5
table BYTE 10h,20h,30h,40h,50h,60h,70h,
80h,90h,0A0h,
0B0h,0C0h,0D0h,
0E0h,0F0h
NumCols = 5
Alternative format:

## Slide 48: Two-Dimensional Table Example
The following 32-bit code loads the table element stored in row 1, column 2:
RowNumber = 1
ColumnNumber = 2
mov ebx,NumCols * RowNumber
mov esi,ColumnNumber
mov al,table[ebx + esi]

## Slide 49: Two-Dimensional Table Example (64-bit)
The following 64-bit code loads the table element stored in row 1, column 2:
RowNumber = 1
ColumnNumber = 2
mov rbx,NumCols * RowNumber
mov rsi,ColumnNumber
mov al,table[rbx + rsi]
table[rbx + rsi]
table[rbx]

## Slide 50: Summary
String primitives are optimized for efficiency
Strings and arrays are essentially the same
Keep code inside loops simple
Use base-index operands with two-dimensional arrays
Avoid the bubble sort for large arrays
Use binary search for large sequentially ordered arrays

## Slide 51: 45 6E 64 65